## Slide 1
ALU DESIGN DOCUMENT
By Priya Ananthakrishnan

## Slide 2: ALU_DESIGN
ALU
CLK
RST
INP_VALID
MODE
CMD
CE
OPA
OPB
CIN
ERR
RES
COUT
G
L
E
OFLOW
Inputs
Outputs
Data pins
Control pins
Pin out diagram of ALU

## Slide 3: ALU Functions
Arithmetic
  Signed/Unsigned addition
  Signed/Unsigned subtraction
Logic
  Logical NOT, AND, OR, EXOR
  For logical operation sign is not considered
Others
  Rotate right/left
  Shift right/left

## Slide 4: PIN LEVEL DESCRIPTION
Serial no | Pin name | Direction | No of bits | Function
1 | OPA | INPUT |  | Parameterized operand 1
2 | OPB | INPUT |  | Parameterized operand 2
3 | CIN | INPUT | 1 | This is the active high carry in input signal of 1-bit
4 | CLK | INPUT | 1 | This is the clock signal to the design and it is edge sensitive
5 | RST | INPUT | 1 | This is the active high asynchronous reset to the design
6 | CE | INPUT | 1 | This is the active high clock enable signal 1-bit
7 | MODE | INPUT | 1 | MODE signal 1 bit is high, then this is an Arithmetic Operation otherwise it is logical operation
8 | INP_VALID | INPUT | 2 | Operands are valid as per below table 00 : No operand is valid 01: Operand A is valid 10: Operand B is valid 11: Operand A and B both valid

## Slide 5: PIN LEVEL DESCRIPTION
Serial no | Pin name | Direction | No of bits | Function
9 | CMD | INPUT |  | Parametrizd (4 bit default) Arithematic Commands CMD = 0 :ADD , 1: SUB, 2: ADD_CIN, 3: SUB_CIN, 4 :INC_A , 5:DEC_A , 6: INC_B 7: DEC_B, 8: CMP, 9: oprand A and B both incr by 1 and then multiplication performed. 10: Operand A left shift by 1 and then multiply with B. Logical Commands CMD = 0: AND, 1: NAND,2: OR, 3: NOR,4: XOR, 5: XNOR, 6: NOT_A, 7: NOT_B, 8: SHR1_A, 9: SHL1_A, 10: SHR1_B,11: SHL1_B,

## Slide 6: PIN LEVEL DESCRIPTION
Serial no | Pin name | Direction | No of bits | Function
9 | CMD | INPUT |  | 12: ROL_A_B if operandB 0000_X000 : output is operandA if operandB 0000_X001 : output is operandA left rotate by 1 if operandB 0000_X010 : output is operandA left rotate by 2 if operandB 0000_X011 : output is operandA left rotate by 3 if operandB 0000_X100 : output is operandA left rotate by 4 if operandB 0000_X101 : output is operandA left rotate by 5 if operandB 0000_X110 : output is operandA left rotate by 6 if operandB 0000_X111 : output is operandA left rotate by 7 if operandB [7:4] any bit is 1 then its error whereas output will be as per [2:0 as mentioned above]

## Slide 7: PIN LEVEL DESCRIPTION
Serial no | Pin name | Direction | No of bits | Function
9 | CMD | INPUT |  | 13:ROR_A_B. if operandB 0000_X000 : output is operandA if operandB 0000_X001 : output is operandA left rotate by 1 if operandB 0000_X010 : output is operandA left rotate by 2 if operandB 0000_X011 : output is operandA left rotate by 3 if operandB 0000_X100 : output is operandA left rotate by 4 if operandB 0000_X101 : output is operandA left rotate by 5 if operandB 0000_X110 : output is operandA left rotate by 6 if operandB 0000_X111 : output is operandA left rotate by 7 if operandB [7:4] any bit is 1 then its error whereas output will be as per [2:0 as mentioned above]

## Slide 8: PIN LEVEL DESCRIPTION
Serial no | Pin name | Direction | No of bits | Function
10 | RES | OUT |  | This is the total parameterized plus 1 bits result of the instruction performed by the ALU.
11 | OFLOW | OUT | 1 | This 1-bit signal indicates an output overflow
12 | COUT | OUT | 1 | This is the carry out signal of 1-bit
13 | G | OUT | 1 | This is the comparator output of 1-bit,which indicates that the value of OPA is greater than the value of OPB
14 | L | OUT | 1 | This is the comparator output of 1-bit,which indicates that the value of OPA is lesser than the value of OPB
15 | E | OUT | 1 | This is the comparator output of 1-bit,which indicates that the value of OPA is equal to the value of OPB
16 | ERR | OUT | 1 | When Cmd is selected as 12 or 13 and mode is logical operation , if 4th ,5th ,6th and 7th bit of OPB are 1, then ERR bit will be 1 else it is high impedance .

## Slide 9: TIMING DIAGRAM
Inputs applied to DUT here
Capture response here
Helps in driver monitor development
Processing operation
Capture response here
3cycle operation